## Slide 1: Shadow Run Dam Corporation (SRDC)
February 2024

## Slide 2: Recap from June 2022
SRDC presented to BOD at June 2022 meeting
Purpose of discussion- state of the SRDC and need of funds
Maintenance Entity (SRDC) needs a more regular source of income to continue to maintain and operate the Dam safety
Property owners = Stakeholders of the SRDC
Currently, SRDC does not collect dues or any type of money from the resident/members
The original seed investment ($100,000) from settlement continues to dwindle each year as our need for capital improvement and maintenance grows

## Slide 3: Settlement Overview
SRHOA created SRDC as maintenance entity to operate and be responsible for the Dam
  Not for profit corporation, the shareholders are landowners of Shadow Run (SRDC formed)
    No landowner can be on both HOA and SRDC
SRDC- Assumes all operational, repair and maintenance responsibilities for the DAM and indemnify and hold harmless SFWMD/County for all operational, repair, and maintenance responsibilities
SRHOA- expressly covenants that it will maintain legal existence as long as Dam is in existence and operated. If the SRDC at anytime fails to maintain legal existence or fails to maintain pertinent regulatory and permitting agency approval, or its legal capacity to own and maintain the DAM separate from the County, in any such event, the SRHOA shall take, at its expense, all actions necessary for the SRHOA to for a successor Florida not for profit corporation to all right and obligations of the maintenance entity
In the event that the SRDC fails or refuses to operate the Dam or be in breach of its obligations the county will have 90 days to notify SRHOA and SRDC and unless failure, refusal, or breach is cured within the 90 days the County will have the right to cause the structure to cease to operate as a dam and at its option will be allowed to dismantle the Dam

## Slide 4: Previous Board of Directors-SRDC
Cathy Scaglione- President
Gregg Reams- Treasurer
John Lindsay
Dawn Tsang
Beatrice Adams
Ashley Predmore

## Slide 5: Inspection Findings
Dam in overall satisfactory condition
  Some Dam features are in fair to poor condition and can present Dam safety and O&M issues
    Findings classified as low, medium and high
    Most finding were list as low priority

## Slide 6: High Priority Findings
 | Finding | Recommendation | Priority
Spillway Works | No Lockout/Tagout procedures are in place for opening spillway. It is not possible to see if there are people fishing downstream of the spillway. | Clear heavy vegetation from area along spillway and immediately downstream of spillway to be able to assess whether people are present prior to opening the spillway. Implement a lockout/tagout procedures for the spillway gate openings to increase safety. | High
 | The ladder used to access the manual gate controls is not fully secured to the concrete structure. | Fully attach ladder to the concrete structure for safety. Note, to manually open the gate, the only access is via a boat. Consider installing a drawbridge catwalk over the plunge pool for easier access to the manual gate controls. | High

## Slide 7
Finding | Recommendation | Priority | Finding
Upstream Slope | Slope oversteepening is present along the length of the shoreline. Slope oversteepening is most prevalent on the right side of the dam, between the spillway and right abutment. | Along the right side of the dam, install riprap with separator fabric to strengthen the slope and prevent further scarping. Place compacted material and regrade the slope to correct the near vertical faces noted near the shoreline. Note that based on photographs and notes provided within previous inspection reports provided to CDM Smith (dated 2018 & 2022), the slope oversteepening along the upstream slope appears to be worsening. Maintain good grass coverage in this area and continuously monitor the slope during regular maintenance and quarterly inspections for additional scarps and continued oversteepening | Medium
 | No shoreline protection is present | Install shoreline protection, such as riprap, along the length of the dam to prevent/slow slope oversteepening due to wave action | 
Downstream Slope | Between the downstream toe of the dam and edge of property, the ground surface is overground with grassy and woody vegetation and small to large trees. The ground surface could not be clearly observed. | Clear grassy and woody vegetation from the downstream toe of the dam to the edge of property (approximately 60 ft downstream of toe). This will increase visibility, improving monitoring for animal burrows, potential seeps, and heave and uplift/blowout. | 
 | Multiple wet areas were identified approximately 35 to 55 ft downstream of the toe, right of the spillway | Monitor the observed standing water for evidence of the migration of fines. | 
Spillway Works | A floating barrier was not present around the reservoir-side perimeter of the spillway | Install a floating barrier within the reservoir to prevent debris blocking the spillway. | 
 | Woody and grassy vegetation is present along the left and right spillway wingwalls. | Clear the woody and grassy vegetation adjacent to the spillway wingwalls to improve visibility and prevent damage to the concrete structure | 
 | Leakage was observed along the seating joint at the top of a circular discharge gate. When the gate is closed, it pulls down on the seal causing it to leak. | Evaluate the potential for replacing the seal around the reservoir gate. Until the seal is replaced, we recommend the gate be opened less frequently due to the potential of additional damage to seal. It is our understanding that the gate is opened monthly and we recommend that it be opened three to four times per year to check operability until the seal is replaced. | 

## Slide 8: Outstanding Items
Fencing and Gates
Piezometer location and replace
Trash Rack and Buoys
Automatic Oiler
Catwalk to Emergency Access
Ladder replacement
Grating of the slopes of the Dam
Vegetation management-
  Toe of the Dam
  Back side of fence
Shoreline reinforcement
  Rip rap needs to be installed
Seal at Dam starting to leak
  Needs replaced

## Slide 9: Shadow Run Dam Corporation (SRDC)